## Slide 1: Operating Systems for Low-End Devices in the IoT- A Survey
Seminário MO809 - 2º Semestre 2016

## Slide 2: Sumário
  Introdução
  Requisitos para um Sistema Operacional para IoT
  Características Importantes de Projeto
  Candidatos a Sistema Operacional para IoT
  OSs relevantes para IoT
  Casos de Estudo
  Referências

## Slide 3: 1. Introdução
O ambiente IoT tipicamente envolve uma vasta gama de elementos heterogêneos, pequenos, baratos, eficientes em energia e com capacidade de comunicação utilizando-se de diferentes protocolos.
Do ponto de vista de HW, pode-se classificar em:
High-End Devices
Low-End Devices

## Slide 4: 1. Introdução
High-End Devices: single-board computers que possuem recursos suficientes para suporte à Sistemas Operacionais(SO) tradicionais como Linux ou BSD. Ex: Raspberry Pi, smartphones.
Low-End Devices: single-board computers que possuem recursos limitados e não suportam Sistemas Operacionais(SO) tradicionais. Ex: Arduino, Econotag, Zolertia Z1, IoT-LAB M3-nodes, Open Mote nodes, TelosB motes, etc...
Examples of low-end IoT devices.
Arduino due.
Zolertia Re-Mote.
IoT-LAB-M3.
Atmel SAM R21.

## Slide 5: 1. Introdução
Low-End Devices são tipicamente bem restritivos em termos de recursos evolvendo: energia, CPU, capacidade de memória.
O IETF definiu recentemente(2014) a RFC 7228 - Terminology for Constrained-Node Networks que define três categorias para Low-End devices:
+-------------+-----------------------+-------------------------+
| Name | data size (e.g., RAM) | code size (e.g., Flash) |
+-------------+-----------------------+-------------------------+
| Class 0, C0 | << 10 KiB | << 100 KiB |
| | | |
| Class 1, C1 | ~ 10 KiB | ~ 100 KiB |
| | | |
| Class 2, C2 | ~ 50 KiB | ~ 250 KiB |
+-------------+-----------------------+-------------------------+
[2] “RFC 7228: Terminology for Constrained-Node Networks."

## Slide 6: 1. Introdução
Aspectos complementares da RFC 7228:
C0 - very constrained sensor-like motes:
  De modo geral não tem recursos suficientes para suportar comunicação direta via internet de maneira segura.
C1 - quite constrained in code space and processing:
  Normalmente não suportam full-stack http, TLS, protocolos de segurança e XML, porém suportam por exemplo CoAP (over UDP).
C2 - less constrained:
  Capazes de suportar protocolos como um notebook ou servidor porém ainda podem tirar benefícios de protocolos eficientes em energia e banda.
Objetivo desta análise  Low-End Devices C1 & C2
[2] “RFC 7228: Terminology for Constrained-Node Networks."

## Slide 7: 2. Requisitos para um SO para IoT
Small Memory Footprint
Support for Heterogeneous Hardware
Network Connectivity
Energy Efficiency
Real-Time Capabilities
Security

## Slide 8: 2. Requisitos para um SO para IoT
A) Small Memory Footprint
  Optimized libraries (potentially crosslayer) providing common IoT functionality, and efficient data structures.
  Identifying the right tradeoff between: 1) performance; 2) a convenient API; and 3) a small OS memory footprint.
  Balance must be found between sensible programming guidelines and coding conventions, which must be observed on one hand, and the high degree of modularity and configurability which is desired to fit a wide range of use cases on the other hand.

## Slide 9: 2. Requisitos para um SO para IoT
B) Support for Heterogeneous Hardware
  Various microcontroller (MCU) architectures and families, including 8-bit (e.g., Intel 8051/52, Atmel AVR), 16-bit (e.g., TI MSP430), 32-bit (ARM7, ARM Cortex-M, MIPS32, and even x86) architectures—64-bit architectures might also appear in the future.
  Some IoT devices provide hundreds of kilobytes of RAM, but no persistent memory to store executable code. (e.g. Redwire Econotag board based on an Freescale MC13224V).
  Some are very limited in terms of RAM, but equipped with a lot of ROM, such as the STM32F100VC ARM Cortex-M3 MCU.
  Wide variety of communication technologies

## Slide 10: 2. Requisitos para um SO para IoT
C) Network Connectivity
  Wide variety of low-power radio technologies (e.g., IEEE 802.15.4, Bluetooth/BLE, DASH7, and EnOcean) but also various wired technologies (e.g., PLC, Ethernet, or several bus systems).
  Contrary to WSN scenarios, it is generally expected that IoT devices seamlessly integrate with the Internet; i.e., can communicate end-to-end with other machines on the Internet.
  A key requirement for a generic OS for the IoT is thus to support heterogeneous link layer technologies and a network stack based on IP protocols relevant for the IoT.

## Slide 11: 2. Requisitos para um SO para IoT
D) Energy Efficiency
  Many IoT devices will run on batteries or other constrained energy sources.
  On a global level, energy efficiency is also required due to the sheer number of IoT devices that is expected to be deployed (tens of billions).
  Unless IoT software makes use of these features (e.g., putting devices into the deepest sleep mode as often as possible), energy efficiency is not achieved.
  Key requirement for OSs for the IoT is:
  1) to provide energy saving options to upper layers and
  2) to make use of these functions itself as much as possible, e.g., by using techniques such as radio duty cycling or by minimizing the number of periodic tasks that need to be executed. For instance, a periodic system timer that schedulers use for time slicing leads to a system that never goes to deep power-down modes and should thus be avoided if possible.

## Slide 12: 2. Requisitos para um SO para IoT
E) Real-Time Capabilities
  Precise timing and timely execution are crucial in various IoT use-cases, e.g., smart health applications such as body area networks (BANs) with pacemakers providing wireless monitoring and control, or in other scenarios including actuators and/or robots in industrial automation contexts, or a vehicular ad-hoc network (VANET).
  An OS that can fulfill timely execution requirements is called a real-time operating
  system (RTOS), and is designed to guarantee worst-case execution times and worst-case interrupt latencies.
  To be an RTOS typically implies that kernel functions have to operate with a deterministic run time. (The Japanese Open Standard for a real-time OS, ITRON, is popular in this field).

## Slide 13: 2. Requisitos para um SO para IoT
F) Security
  Some IoT systems are part of critical infrastructure or industrial systems with life safety implications.
  Since they are connected to the Internet, IoT devices are in general expected to meet high security and privacy standards.
  Beyond the overarching trust management challenge, IoT security challenges includes data integrity, authentication, and access control in various parts of the IoT architecture.
  A requirement (and challenge) for an OS for the IoT is to provide the necessary mechanisms (cryptographic libraries and security protocols) while retaining flexibility and usability.
  Since software with a certain degree of complexity can never be expected to be 100% bug-free, it is crucial to provide mechanisms for software updates on already-deployed IoT devices.

## Slide 14: 3. Características Importantes de Projeto
Technical Properties
  General Architecture and Modularity
  Scheduling Model
  Memory Allocation
  Network Buffer Management
  Programming Model
  Programming Languages
  Driver Model and Hardware Abstraction Layer
  Debugging Tools
  Feature Set
  Testing
Nontechnical Properties
  (Open) Standards
  Certification
  Documentation
  Maturity of the Code
  License of the Code
  Provider of the OS

## Slide 15: 3. Características Importantes de Projeto
Technical Properties
  General Architecture and Modularity
    Exokernel approach, a microkernel approach, a monolithic approach, or a hybrid approach
    Synopsis: One has to choose between the more robust and more flexible microkernel or a less complex and more efficient monolithic kernel—or go for a hybrid approach

## Slide 16: 3. Características Importantes de Projeto
Technical Properties
  Scheduling Model
    1) preemptive schedulers or 2) nonpreemptive (or cooperative) schedulers.
    In many cases, a preemptive scheduler requires a periodic timer tick, sometimes called a systick, to assign time slices to each task.
    Synopsis: A preemptive scheduler assigns CPU time to each task, while the different tasks have to yield themselves in the cooperative model.
  Memory Allocation
    1) Static memory allocation or 2) dynamic memory allocation
    Synopsis: Static memory allocation introduces some memory overhead due to over-provisioning and results in less flexible systems, while dynamic memory allocation leads to a more complex system and may conflict with real-time requirements.

## Slide 17: 3. Características Importantes de Projeto
Technical Properties
  Network Buffer Management
    1) memcpy() or 2) passing of pointers between the several layers
    Synopsis: Memory for packet handling in the network stack may be allocated by each layer or passed as a reference between the layers.
  Programming Model
    1) event-driven systems or 2) multithreaded systems
    Synopsis: Event-driven systems can be more memory efficient, while multithreading systems eases the application design.

## Slide 18: 3. Características Importantes de Projeto
Technical Properties
  Programming Languages
    1) standard programming language, typically ANSI C or C++ or 2) an OS-specific language or dialect.
    Synopsis: Standard programming languages simplify portability and enable the use of well-known development tools. OS-specific languages and language extensions can increase the system performance and safety.
  Driver Model and Hardware Abstraction Layer
    Synopsis: A well-defined hardware abstraction layer and driver model can significantly improve the system design, but introduces a certain amount of overhead—either in terms of lines of code or in terms of runtime overhead.

## Slide 19: 3. Características Importantes de Projeto
Technical Properties
  Debugging Tools
    Synopsis: Using standard programming languages in general allows for using standard debugging tools, but hardware limitations may pose the need for other, simpler debugging facilities via serial output or even LED blinking.
  Feature Set
    kernel and higher level functionalities.
    the kernel (multithreading support or not) provides a scheduler, a model for tasks, mutual exclusion (mutex), and other forms of synchronization, and timers.
    On higher layers: system libraries, a shell, logging, cryptographic functions, or network stacks. Additional features: over-the-air updates, dynamic loading and linking, and libraries for lightweight encryption and decryption
    Synopsis: The overall feature set of an OS may be described by the size of its API.
  Testing
    Synopsis: The distributed nature and constraints of the hardware makes thorough testing a challenging, but crucial task.

## Slide 20: 3. Características Importantes de Projeto
B) Nontechnical Properties
  (Open) Standards
    Synopsis: The use of standards improves portability and interoperability.
  Certification
    Synopsis: Especially for the deployment in industrial and safety-critical applications, certification of the entire software running on an IoT system might be mandatory.
  Documentation
    Synopsis: In order to make the best use of an OS and ease application design, a complete and comprehensible documentation is required.

## Slide 21: 3. Características Importantes de Projeto
B) Nontechnical Properties
  Maturity of the Code
    Synopsis: In many cases, thorough testing and wide deployment in commercial applications is a better indicator for the maturity of an OS than the mere age of the project or certifications.
  License of the Code
    1) nonfree; 2) permissive open source (BSD, Apache); and 3) copyleft licenses(GPL)
    Synopsis: Open source—particularly copyleft licenses—may not always be the first choice of industry, but offers chances for higher code quality and more secure code due to the increased numbers of contributors and reviewers.
  Provider of the OS
    Synopsis: The way of distribution and degree of support for an OS is highly dependent on its license.

## Slide 22: 4. Candidatos a Sistema Operacional para IoT
The goal in this section is exhaustiveness rather than in-depth analysis.
We will distinguish between 1) open source OSs; 2) closed source OSs; and 3) other software libraries or middleware for the IoT.
If not mentioned otherwise, all OSs are written in the C programming language, while some hardware-specific parts may be implemented in assembly language.

## Slide 23: 4. Candidatos a Sistema Operacional para IoT
Open Source OSs
  Contiki
  RIOT
  FreeRTOS
  TinyOS
  OpenWSN
  nuttX
  eCos
  mbedOS
  L4 Microkernel Family
  uClinux
  Android and Brillo
  Others: ChibiOS/RT, CooCox CoOS, ERIKA Enterprise, MansOS, NanoQplus,nanoRK, Nue/OS, RTEMS

## Slide 24: 4. Candidatos a Sistema Operacional para IoT
B) Closed Source OSs
  ThreadX
  QNX
  VxWorks
  Wind River Rocket
  PikeOS
  embOS
  Nucleus RTOS
  Sciopta
  uC/OS-II
  U-velOSity
  Windows CE
  LiteOS Huawei

## Slide 25: 4. Candidatos a Sistema Operacional para IoT
C) Others Softwares
  Arduino
  Espruino
  Node OS

## Slide 26: 4. Candidatos a Sistema Operacional para IoT

## Slide 27: 4. Candidatos a Sistema Operacional para IoT

## Slide 28: 5. OSs relevantes para IoT
In the following, we will focus on open source Oss:
  security and trustworthiness through transparency of code running on IoT devices and
  the anticipated need to spread development costs between multiple parties (similarly to Linux).
OSs can be categorized by their architectural concept into three main categories:
  Event-driven OSs
  Multithreading Oss
  Pure RTOSs.

## Slide 29: 5. OSs relevantes para IoT
Event-driven OSs
  Target  domain of WSNs
  Triggered by an (external) event, typically signaled by an interrupt.
  Kernel  an infinite loop handling all occurring events within the same context.
  Such an event handler typically runs to completion.
  Efficient in terms of memory consumption and low complexity
  Substantial constraints to the programmer e.g., not all programs are easily expressed as a finite state machine.
  Examples: Contiki, TinyOS, and OpenWSN.
  Wider deployment  Contiki
Notes:   Common approach for OSs initially developed to target the domain of WSNs
  The key idea of this model is that all processing on the system is triggered by an (external) event, typically signaled by an interrupt.
  As a consequence the kernel is roughly equivalent to an infinite loop handling all occurring events within the same context.
  Such an event handler typically runs to completion.
  While this approach is efficient in terms of memory consumption and low complexity, it imposes some substantial constraints to the programmer e.g., not all programs are easily expressed as a finite state machine.
  OSs that fall in this category include Contiki, TinyOS, and OpenWSN.
  Because of its wider deployment and use (to the best of our knowledge), Contiki is arguably a good representative of this category of OS.

## Slide 30: 5. OSs relevantes para IoT
Multithreading OSs.
  Traditional approach for most modern OSs.
  Each thread runs in its own context and manages its own stack.
  Scheduling has to perform context switching between the threads.
  Stack memory can usually not be shared between threads.
  Memory overhead due to stack over-provisioning
  Runtime overhead due to context switching.
  Examples: RIOT, nuttX, eCos, or ChibiOS.
  Stronger focus on IoT requirements  RIOT
Notes:   Multithreading is the traditional approach for most modern OSs (e.g., Linux), whereby each thread runs in its own context and manages its own stack.
  With this approach, some scheduling has to perform context switching between the threads. Each process is handled in its own thread and can, in general, be interrupted at any point. Stack memory can usually not be shared between threads.
  Multithreading OS usually introduces some memory overhead due to stack over-provisioning and runtime overhead due to context switching.
  OSs that fall in this category include RIOT, nuttX, eCos, or ChibiOS.
  Because of its stronger focus on IoT requirements (to the best of our knowledge), RIOT is arguably a good representative of this category of OS.

## Slide 31: 5. OSs relevantes para IoT
Pure RTOSs.
  Focuses (goal of fulfilling realtime guarantees)  industrial/commercial
  Importance  formal verification, certification, and standardization
  Checking and formal verification  imposes strict constraints for developers.
  Restrictions  rather inflexible and difficult porting
  Examples: FreeRTOS, eCos, RTEMS, ThreadX, and a collection of other commercial products (generally closed source).
  Wider use in various environments  FreeRTOS
Notes:   An RTOS focuses primarily on the goal of fulfilling realtime guarantees, in an industrial/commercial context.
  In this context, formal verification, certification, and standardization are usually of crucial importance.
  To allow model checking and formal verification, the programming model used in such OSs typically imposes strict constraints for developers.
  These restrictions often makes the OS rather inflexible and porting to other hardware platforms may become rather difficult.
  OSs for IoT devices that fall in this category include FreeRTOS, eCos, RTEMS, ThreadX, and a collection of other commercial products (generally closed source).
  FreeRTOS is to the best of our knowledge the most prominent open source RTOS for IoT devices, due to its wider use in various environments.

## Slide 32: 6. Casos de Estudo - Contiki (Event-driven)
developed by Adam Dunkels in 2003
8-bit AVR, 16- and 20-bit MSP430, and 32-bit ARM Cortex M3
Architecture: monolithic - core system and a set of processes that are combined into a single system image during compilation. All processes share the same memory space and privileges with the core system
Scheduling: cooperative thread scheduling
Memory allocation: primarily - static allocation. Library with simplified memory management (memb and mmem). 3rd party supplies dynamic allocation modules (standard C malloc)

## Slide 33: 6. Casos de Estudo - Contiki (Event-driven)
Network connectivity:
  uIP stack, which was first developed as a standalone stack (6LoWPAN, IPv4, IPv6, IPv6 neighbor discovery, IPv6 multicasting, RPL, TCP, and UDP.
  light-weight Rime stack, which is oriented toward sensor network
Network buffer management: module called Queuebuf which allocates packet buffers from a static pool of memory
Programming model: Protothreads, which is a sort of light-weight, cooperative threading concept similar to continuations

## Slide 34: 6. Casos de Estudo - Contiki (Event-driven)
Programming language: C, but there exist runtime environments Java and Python
Hardware abstraction layer: hardware-specific functionality is put in separate components and Contiki platform implements a common API for using that hardware as clocks, radio drivers, and sensors.
Debugging facilities: Cooja/MSPsim simulator, which combines network simulation with cycle-accurate emulation of the hardware platforms.
Feature set: a shell, a file system, a database management system, runtime dynamic linking, cryptography libraries, and a finegrained power tracing tool.

## Slide 35: 6. Casos de Estudo - Contiki (Event-driven)
Testing facilities: unit testing, regression testing, and full system integration testing. Contokii code contributions are automatically tested with a test suite using Travis CI
Standards: 6LoWPAN and RPL.
Certification: IPv6 Ready Logo Program - silver certification.
Documentation: The source code is documented using the open-source Doxygen tool, and other things such as tutorials and high-level technical descriptions are provided through a project Wiki.

## Slide 36: 6. Casos de Estudo - Contiki (Event-driven)
Maturity of the code:
  The core parts have reached a high maturity of the code but there are also less used experimental parts.
  Along with TinyOS, Contiki has become one of the most well-known and widely used OSs for WSN.
License: All source code in Contiki must have a three-clause BSD license or another license with similar terms.

## Slide 37: 6. Casos de Estudo - Contiki (Event-driven)
Provider:
  Contiki is developed by a large community of professional developers, researchers, and hobbyists.
  The development is organized around a GitHub repository.
  The source code is maintained by a merge team, which review incoming code contributions from the Contiki community, and make larger decisions such as architectural changes and release cycles

## Slide 38: 6. Casos de Estudo – RIOT (Multithreading)
Development was launched in 2013, based on a microkernel architecture inherited from FireKernel
IoT hardware support (8-, 16-, 32-bit MCUs)
Architecture: microkernel RTOS architecture with full multithreading, efficient context switching(100 CPU cycles on an ARM), IPC (blocking and nonblocking) and a small thread control block (TCB) (46 bytes on 32-bit platforms).
Scheduling: Preemptive tickless scheduler. No pending tasks  RIOT will switch to the idle thread, which can use the deepest possible sleep mode.
Memory allocation: dynamic and static memory allocation. Only static methods are used within the kernel, which enables RIOT to fulfill deterministic requirements.

## Slide 39: 6. Casos de Estudo – RIOT (Multithreading)
Network connectivity: The gnrc network stack is based on standard IP protocols, supporting 6LoWPAN, IPv6, RPL (nonstoring and storing mode), UDP, and CoAP, implemented in a modular fashion, leveraging generic, well-defined interfaces and IPC
Network buffer management: gnrc, within which packets, headers, and other networking meta data is stored in a centralized network buffer structure, whereby only pointers are being passed between the layers.
Programming model: classical multithreading concept with a memory-passing IPC between threads

## Slide 40: 6. Casos de Estudo – RIOT (Multithreading)
Programming language: C, C++
Hardware abstraction layer: peripheral interfaces as well as for networking, sensor, and actuator devices.
Debugging facilities:
  RIOT is written in ANSI C  established debugging tools can be used, such as GDB and Valgrind.
  Also provides a way to run instances of the OS as processes on Linux or Mac OS.
Feature set: shell, various crypto libraries, or sophisticated data structures.

## Slide 41: 6. Casos de Estudo – RIOT (Multithreading)
Testing facilities:
  Cooja can also be used to simulate platforms supported by this simulator. RIOT provides a set of unit tests and applications for smoke and regression
  Tests can also be carried out on a number of open testbeds supported by RIOT, e.g., IoT-LAB or DES-Testbed
Standards: open standard protocols specified by bodies such as IETF, IRTF, W3C, OMA, and the like.
Certification: no certification efforts have been conducted on the code base, to date.
Documentation: on the API level as well as on the architectural level.

## Slide 42: 6. Casos de Estudo – RIOT (Multithreading)
Maturity of the code:
  The kernel can be considered mature, as only minor bugs have been revealed during the last years.
  Other parts of RIOT (e.g., the network stack) are comparably younger and still subject to changes, e.g., as a result of co-evolving with new IoT protocol standards.
License: LGPL.
Provider:
  The source code is openly available on GitHub.
  RIOT’s master branch on GitHub is currently maintained by several tens of developers that are in charge of reviewing and merging external contributions that are provided through pull requests

## Slide 43: 6. Casos de Estudo - FreeRTOS (real-time)
Originally developed by Richard Barry in 2002, FreeRTOS is now maintained and distributed by Real Time Engineers Ltd.
FreeRTOS is deployed in various industrial/commercial environments.
Architecture: microkernel RTOS architecture with multithreading. fairly simple architecture, as it comprises of only four C files and is more a threading library than a full-fledged OS.
Scheduling: Preemptive, priority based round-robin and optionally tickless scheduler.
Memory allocation: five different memory allocation schemes.

## Slide 44: 6. Casos de Estudo - FreeRTOS (real-time)
Network connectivity:
  does not provide any networking capabilities.
  Real Time Engineers Ltd. offers an official FreeRTOS+TCP add-on supporting an Ethernet-based IPv4 stack with support for UDP, TCP, and supporting protocols.
Network buffer management: FreeRTOS+TCP, e.g., can be configured to use a statically pre-allocated buffer or to allocate buffer space dynamically on-demand
Programming model: multithreading programming model with statically instantiated tasks.

## Slide 45: 6. Casos de Estudo - FreeRTOS (real-time)
Programming language: C, C++
Hardware abstraction layer: FreeRTOS does not define a portable driver model or MCU peripheral abstraction interfaces.
Debugging facilities: depends on third-party solutions
Feature set: scheduling, threading and SW timers.
Testing facilities: depends on third-party solutions

## Slide 46: 6. Casos de Estudo - FreeRTOS (real-time)
Standards: FreeRTOS emphasizes on strict coding standards, quality management.
Certification: FreeRTOS has become part of various formal verification efforts. SafeRTOS has been certified by TV SD as IEC 61508 compliant and against the EN 62304 and FDA 540(k) regulatory requirements.
Documentation: Real Time Engineers Ltd. provides extensive documentation in terms of books, trainings, and commercial support.

## Slide 47: 6. Casos de Estudo - FreeRTOS (real-time)
Maturity of the code: no information
License: modified GPL.
Provider: Real Time Engineers Ltd

## Slide 48: 7. Referências
[1] hahm15 – Hahm, Oliver, et al. "Operating systems for low-end devices in the internet of things: A survey." (2015).
[2] Bormann, C., M. Ersue, and A. Keranen. "RFC 7228: Terminology for Constrained-Node Networks." (2014).

## Slide 49: FIM
810043 – Amaury Mausbach Filho
Seminário #5